--*======================================================================*--

        ================
        =  Promizer II =
        ================ v2.0 by mc68000 of MASQUE/T.R.S.I.

	copyright notice :
		
	This tool is freeware, that means that you can use it for
	any kind of production, but not sell it !!! Copyright 1993 
	by Frank Hülsmann !!!

--*======================================================================*--

        Instructions :
	
        What makes the Pomizer ???
	
	Well ... very simple ... it plays protracker (& clones)
	modules	in a fast way - try it out. It handles all 
	effects of this	cool tool (i hope ...) in the right way
	and it handles the finetune option in a total different 
	(but much faster) way then the tracker. It also included 
	a pattern packer, that makes music-ripping much harder
	(i found no ripper, that could ripp promizer v1.x modules) !!!
	
--*======================================================================*--

	How to use it ???
	
	I think, that i don't must write any words about the handling.

--*======================================================================*--

	But how can i replay the songs in own productions ???

	Very easy ... the Promizer II tool links the replayer routine
	before the sound data. Just call it on this way :


		Init a tune :

		moveq	#x,d0
		moveq	#y,d1
		jsr	sound_base
	
			x = 0 -> use rasterline dma wait routine
			x = 1 -> use cia-b interupt (much faster)
			y = 0 -> don't fade the tune in
			y = 1 -> fade the tune in
			
			after this you get a pointer on several 
			player buffers/tables in d0 :

			offset :	buffer/table :

			0		periodtables (16x with finetune)
			1200		chan1temp (same struct like pt)
			1248		chan2temp (same struct like pt)
			1296		chan3temp (same struct like pt)
			1344		chan4temp (same struct like pt)
			1610		counter (.b)
			1394		songposition (.w) (pt pos *2 !!!)
			1611		songspeed (.b)
			1392		patternposition (.w)
			1396		samplestart table (31x longwords)
	
		Replay it (each vertical blank) :

		moveq	#mask,d0
		moveq	#x,d1
		jsr	sound_base+4

			mask   = what voices should i play ??

			mask is a 4-bit unsigned value :
			
			%1111  = play all 4 voices
			%0001  = play only voice 1
		 	%1010  = play voices 2 & 4

			x = 1 -> fade tune out
			x = 0 -> no outfading

			!!! Attention : don't use any effect commands
                  			in a switched off voice !!!
			
		End tune (after that, don't call the player again !!!) :

		jsr	sound_base+8
		
		If you want to wait for the out-fading, then call

		jsr	sound_base+12

--*======================================================================*--

EXAMPLE SOURCECODE (CUT & SAVE IT) - VERY SHORT VERSION :

		section	"play_it",code_p

; INIT TUNE

start		move.w	$dff01c,d5
		or.w	#$8000,d5
		move.l	$6c.w,d6

		move.w	#$7fff,$dff09a

		lea	songbase,a0
		moveq	#1,d0			;use cia
		moveq	#1,d1			;fade in
		jsr	(a0)			;init tune

		move.l	#newint,$6c.w
		move.w	#$c020,$dff09a

; WAIT LEFT BUTTON

.loop		btst	#6,$bfe001
		bne.b	.loop

		move.b	#1,fade_flag		;start fading out

		jsr	12(a0)			;wait for fading
		move.w	#$7fff,$dff09a
		jsr	8(a0)			;stop playing

		move.l	d6,$6c.w
		move.w	d5,$dff09a
		rts

; INTERUPT

newint		movem.w	d0-d1,-(a7)
		move.w	#%1111,d0		;all voices
		move.b	fade_flag(pc),d1
		jsr	songbase+4
		move.w	#$20,$dff09c
		movem.w	(a7)+,d0-d1
		rte

fade_flag	dc.b	0

		section	'song',data_c
songbase	incbin	'mod.test'
		
--*======================================================================*--

	What's new from the last version ???

	- completly new replayer and optimizer
	- fader included
	- voice mask included
	- i killed the "multi song" function, because i never used it ...
          if you want to use it, write to me - if there are enough 
	  requests, i include it ....
	- no player-stand-alone-module - if you want to play your
	  protracker tunes in multitasking, use one of the mt-player
	  (like chamälion player, noiseplayer, ...)

--*======================================================================*--

	Planed updates :
	
	- faster replayer (this player isn't very optimzed ...)
	- new and better packer
	- more extras

--*======================================================================*--

 		contact me for bug reports, or just for fun :
		i don't answer any swapper request !!!!

		mc68000/masque/trsi
	
		Frank Hülsmann
		Timmerscheidtstr.14
		4400 Münster		  _____________    _____________
		Germany			 / ___    ____ \  /   _________/\
					 \/\_//  /\___\ \//  /\___/   /\/
					  \///  /   ____/____    //  / /
					   /.  /\\  \___\___//  /.  / /
					  /___/ /\___\/________/___/ /
					  \___\/  \___\________\___\/           

--*======================================================================*--